## Slide 1
By
Dr. Wazir Muhammad Laghari
Electrical Engineering Department
BUET, Khuzdar
Computational Methods in
Power System Analysis
Lecture-6 Three-phase

## Slide 2: Need/Advantages of 3- supply Power
Voltage produced by a 1 supply is very less and not enough to supply practical industrial loads.
Industrial heavy loads require poly phase supply (Phase means branch circuit or winding while poly means many).
In poly phase system there are many independent AC voltages present simultaneously (depends on no: of phases).
In 3 system, the magnitudes and frequencies of a.c. voltages are same and a phase difference of 360/3 = 1200 with respect to each other.
The output of 3 machine is always greater than the o/p of 1 machine of same size.
Transmission of 3 power is very much economical as it needs less copper or less conducting material as compared to 1 power.
Rotating Magnetic Field can be generated in 3 supply, hence 3 machines are self starting, with the help of 1 supply we can not produced rotating magnetic field, so 1 machines are not self starting.
In 3 supply give rise to 3 of 1 supplies, but vice-versa is not possible.
Rectifier DC output voltage is smoother (having less ripple) if number of phases are increased at the supply side

## Slide 3: 3 Power
Phase
Line
2) Reactive Power:
Phase
Line
1) Active/Real/True Power:
3) Apparent Power:
Phase
Line
Power Triangle of Inductive Circuit
Power Triangle of Capacitive Circuit
Power factor of capacitive ckt nature is leading

## Slide 4
In Star connected load Vphase equal to line voltage VL divided by root 3
Relationship between PStar and PDelta
VL is same for Y and  Load
Zph is same for Y and  Load
FOR STAR LOAD

## Slide 5
Relationship between PStar and PDelta
FOR DELTA LOAD
In Delta connected load Vphase equal to line voltage VL
3

## Slide 6
1-phase having one voltage source.
Line is connected with load.
Single Phase And Three Phase Voltages
If we connect three single phase circuits
First one is Va, Vb and Vc.
This way we can connected with three different loads by three sources.
Instead of 6 wires of previous diagram 3 for going current from source to load and 3 paths of returning current from load to source so total is 6 but now we reduced into 4.
So 3 for current going from source to load and one for all currents going back to source, so this way reduce six wires to 4 wires.

## Slide 7: 3 phase, 4 wire system And Verify Neutral has Zero Current
3 phase voltages have same amplitude in balanced system but different in phase .
First is 0, second is 120 and 3rd is 240 phase difference.
Diagram for generating 3phase, one is rotor and there is 3 sets of coils a to a’, b to b’ and c to c’ and there is 120 degree apart.
Zero current flowing in the neutral wire, so no need to provide neutral wire because loads are balanced, but practically loads are not balanced so due to this neutral wire is available there.

## Slide 8: 3-phase 4 wire system: re-design architecture
A set of balanced three-phase voltages consists of three sinusoidal voltages that have identical amplitudes and frequencies but are out of phase with each other by exactly 1200.
The phases are referred as a, b and c. The a-phase is taken as the reference.
BALANCED THREE-PHASE VOLTAGES

## Slide 9: BALANCED THREE PHASE SOURCE CONNECTED VOLTAGES
There will be two possibilities of connections:
1) Star or Y Connected
2) Delta Connected.
In Y configuration has neutral wire, but in Delta has no neutral wire
Source Connection Load Connection

## Slide 10: ALL POSSIBLE CONNECTIONS OF THREE PHASE
Both the three phase source and the three phase load can be connected either Wye or DELTA.
We have 4 possible types of connections
  Y-Y Connection (Source is Star Connected and Load is also in Star Connected)
  Y- Connection
  -  Connection
  -Y Connection
Mostly Y connected sources are more common.
And Balanced  connected load is more common.
Source Load

## Slide 11: BALANCED LOAD
For a balanced delta connected load:
Za = Zb = Zc = Z
For a balanced wye connected load:
Z1 = Z2 = Z3 = ZY
A Balanced Load is one in which the phase impedances are equal in magnitude and in phase.
The following formulas are derived from wye-delta conversion:
(Delta impedance equal
to 3 times Y impedances)

## Slide 12: Symmetrical And Unsymmetrical System
In a three phase system the three voltages are of same magnitude and frequency which is displaced from each other by 1200 phase angle it is defined as symmetrical system.
Symmetrical /Balanced System
Un-Symmetrical /Unbalanced System

## Slide 13: PHASE SEQUENCE
No rotation
Phase sequence or Phase rotation is the order in which the voltage waveforms of Three Phase AC source reach their respective peaks. OR
The sequence in which the voltages in 3-phase supply reach their maximum possible values is called Phase Sequence.
Generally the phase sequence is R-Y-B or A-B-C or a-b-c.
The need of phase sequence is very important in determining the direction of rotation of a.c motors.

## Slide 14: Phase Sequence of a Balanced Three Phase Voltages

## Slide 15: Line Voltage = root 3 times Phase Voltage with angle of 300

## Slide 16
EXAMPLE: Determine the phase sequence of the set of voltages
SOLUTION

## Slide 17
EXAMPLE:
Given that
SOLUTION:

## Slide 18: LINE VOLTAGE AND PHASE VOLTAGE
Line voltage is the voltage measured between any two lines in a three-phase circuit.
Phase voltage is the voltage measured from neutral to line is called Phase voltage.
Phase voltage refers to the voltage measured across any one component (source winding or load impedance) in a balanced three-phase source or load with reference to neutral.
Assign V-line and V-phase
Phase Voltage is different in case of Delta, because there is no neutral available, so phase voltage is the voltage across any one load, it is also called a line voltage. In Delta connected line voltage = phase voltage.

## Slide 19: LINE VOLTAGE AND PHASE VOLTAGE

## Slide 20: LINE CURRENT AND PHASE CURRENT
Line current is the current through any one line between a three-phase source and load.
Phase current is the current through any one component comprising a three-phase source or load.

## Slide 21: EXAMPLE: Calculate the currents in YY connected System
=32.01638.660
SOLUTION

## Slide 22
Home Work: Calculating the Currents in a YY System
Find Ia ,Ib , Ic
120300

## Slide 23: END